## Slide 1: Embedded Speech to Text William Pickering

## Slide 2: Order of Execution
Understand the Goal and Scope of the Project
Understand Requirements
  Frequency range of source
  Time allowed to collect and process data
Determine how to Implement
  The format of the data to collect
  How to collect the data and the rate
  How to process the data
  How to compare the data
  How to output the results
Implement, Test, and Revise

## Slide 3: Project Description
Goal of the Project
  Build experience
    Sampling data at specific intervals
    Using Fast Fourier transform (FFT) algorithms
    Using direct memory access (DMA)
  A particle device to use in future projects
The device would
  Receive input from a human voice
  Convert phonic sounds to a string of characters
  Use a spell checker algorithm to convert the string of characters to a list of valid words
  Output the words as if being typed form a keyboard
CP2102
(TTL UART to USB)
STM32F446VET6
MAX9814
(Microphone Amplifier)
PC

## Slide 4: Requirements
Analyze the human voice.
  Between 0.2 kHz – 6 kHz
  Used: https://www.compadre.org/osp/pwa/soundanalyzer/ to confirm
Finish processing the current phonic before the next one starts
  Around 83ms
Amount of time a phonic is pronounced for | 
Capture Data | Process data
0ms
83ms
31.25ms
https://av-info.eu/index.html?https&&&av-info.eu/audio/speech-level.html

## Slide 5: How to Sample at a Desired Rate
Implementation Options
  Needed to sample 2x the frequency of the human voice (0.2 kHz – 6 kHz)
  Set up a timer interrupt
  Set up DMA and adjust the analog digital convertor (ADC) clock

## Slide 6: Processing the Data - First Iteration
Setting up DMA in a Ping-Pong style
  An interrupt is called, when the buffer is half-full and can be processed while the other half is being filled.
  Data needs to be processed before being overwritten
Complex FFT Library: https://www.kurims.kyoto-u.ac.jp/~ooura/fft.html
  Pros:
    Simple to integrate
    Able to run on a desktop environment
    Open Licensing
    Comparable speeds to KissFFT and better than FFTW
  Cons:
    Every other output in the array was imaginary, required post-processing
    Size of the array must be 2^n
    Array size value over 2,048 would take too long to process

## Slide 7: Comparing the Data - First Iteration
Created a HashMap
  Key: 64-bit unsigned int
  Value: char array
Each bit of the key represented a range of frequencies
  [0]: 0 – 94hz
  [1]: 95 – 189hz
  …
  [63] 5985 – 6079hz
Set the bit if there is a maximum in the corresponding range.
/ĕ/ [10101000…]

## Slide 8: Revisions
Sampling at too high of a frequency (12 kHz)
  Resulted in too large of a step size (~200 Hz) of the FFT output
  Solved by decreasing the sampling rate
ADC outputs 12-bits while UART transmitting takes 8-bit
  Solved by bit shifting into a 16-bit unsigned int

## Slide 9: Future Work
Implement finding maximums
Implement the phonics HashMap onto an SD card
Use a real FFT algorithm rather than a complex FFT
Test out the performance of the CMSIS Real FFT library
Test recording all data to a buffer then performing the FFT